## Slide 1: Resumable LAN File Transfer Protocol
Guide: [Guide Name]
Designation: [Guide Designation]
Department of Computer Science & Engineering
B.M.S. College of Engineering
[Student 1 Name] [USN] | [Student 2 Name] [USN]
[Student 3 Name] [USN] | [Student 4 Name] [USN]
Notes: Arpana

## Slide 2: OUTLINE
Introduction
Problem Statement
Literature Survey and Comparison
References
Notes: ap

## Slide 3: Introduction
File sharing moves lab, backup and personal files between nearby computers.
TCP carries an ordered byte stream. The application defines messages and file completion.
This project proposes binary frames, bounded chunks, SHA-256 verification and resume.
Domain: Computer Networks. SDG alignment: SDG 9, reliable digital infrastructure.
Notes: Niha

## Slide 4: Problem Statement
A basic copy can move bytes without defining transfer messages or file-level completion.
If TCP disconnects, a sender may repeat work unless both peers record progress.
The receiver needs a whole-file check before treating the staged copy as complete.
Research question: how do streaming, verification and resume affect correctness, recovery and throughput on a LAN versus one-shot TCP?
Objective: implement and measure a minimal version. No measured results exist yet.
Notes: Anusree

## Slide 5: Recent File Transfer Tools
Eberle, Nölp and Oden present p2p-copy, a Python transfer tool for restricted networks [1].
It uses a pairing code and secure WebSockets through a relay, with encryption, compression, integrity checks and resume.
The paper reports data-center benchmarks and comparisons with rsync.
Relevance: these features can coexist. Its Internet and relay setting differs from our proposed LAN test.
Notes: Source: Eberle, Toni, Klaus Nölp, and Lena Oden. “p2p-copy: A secure high-performance file transfer tool for restricted network environments.” SoftwareX, 35 (2026), article 102882. https://doi.org/10.1016/j.softx.2026.102882. The selected study is Internet/data-center focused, so its claims are not treated as LAN results.

## Slide 6: Transfer Performance on High-Speed Links
Kempf et al. evaluate QUIC implementations on dedicated 10 Gbit/s links [2].
Reported QUIC goodput varied widely. TCP reached about 8 Gbit/s under the tested conditions.
Operating-system buffers, CPU, packet processing and NIC offload influenced measured performance.
Use for method: record software, hardware and network setup. This is not an application-level LAN comparison.
Notes: Source: Kempf, Marcel, Benedikt Jaeger, Johannes Zirngibl, Kevin Ploch, and Georg Carle. “QUIC on the Fast Lane: Extending Performance Evaluations on High-rate Links.” Computer Communications, 223 (2024), pp. 90–100. https://doi.org/10.1016/j.comcom.2024.04.038. The article reports implementation-dependent QUIC goodput and TCP results on dedicated high-rate links.

## Slide 7: TCP Performance Measurement
Fesl et al. publish a dataset comparing 17 TCP congestion-control variants [3].
The measurements use one iperf3 TCP flow on a 16 Mbps link and 50 repeats per variant.
The dataset contributes reusable transport measurements and a repeatable comparison method.
Difference: it does not study application framing, whole-file verification or resume after disconnect.
Notes: Source: Fesl, Jan, et al. “Data center TCP dataset.” Data in Brief, 54 (2024), article 110522. https://doi.org/10.1016/j.dib.2024.110522. The article describes 17 TCP variants, 18 metrics and 50 measurements per variant. Its test link was capped at 16 Mbps, as described in the paper’s data description.

## Slide 8: Delta Compression for Backups
Zhang et al. propose FaRE, a redundancy-elimination scheme for inline backups [4].
It estimates chunk fragmentation and chooses between sequential deduplication and local delta compression.
The design balances storage efficiency, restoration performance and backup throughput by limiting extra I/O.
Relevance: similar-file delta transfer is a stretch goal after basic correctness and resume are demonstrated.
Notes: Source: Zhang, Yucheng, et al. “A fragmentation-aware redundancy elimination scheme for inline backup systems.” Future Generation Computer Systems, 156 (2024), pp. 53–63. https://doi.org/10.1016/j.future.2024.03.004. FaRE is designed for backup storage, not direct peer-to-peer LAN transfer.

## Slide 9: Comparison of Existing Approaches
p2p-copy: secure Internet transfers with integrity checks and resume [1].
Transport studies: TCP and QUIC rates vary with implementation, operating system and network settings [2, 3].
FaRE: delta compression reduces repeated backup data but adds storage work [4].
Proposed MVP: one TCP file at a time, bounded chunks, SHA-256 and receiver-reported resume offset.
Review gap: the selected papers do not test this feature set against one-shot TCP on a simple LAN.
Notes: The project gap is limited to the selected papers and the proposed test setting. This is not a claim that no prior LAN file-transfer research exists, and it is not a novelty claim. The comparison is a plan; the prototype and results do not yet exist.

## Slide 10: References
[1] Eberle, T., Nölp, K. and Oden, L., “p2p-copy: A secure high-performance file transfer tool for restricted network environments,” SoftwareX, vol. 35, art. 102882, 2026. doi:10.1016/j.softx.2026.102882.
[2] Kempf, M., Jaeger, B., Zirngibl, J., Ploch, K. and Carle, G., “QUIC on the Fast Lane: Extending Performance Evaluations on High-rate Links,” Computer Communications, vol. 223, pp. 90–100, 2024. doi:10.1016/j.comcom.2024.04.038.
[3] Fesl, J. et al., “Data center TCP dataset,” Data in Brief, vol. 54, art. 110522, 2024. doi:10.1016/j.dib.2024.110522.
[4] Zhang, Y. et al., “A fragmentation-aware redundancy elimination scheme for inline backup systems,” Future Generation Computer Systems, vol. 156, pp. 53–63, 2024. doi:10.1016/j.future.2024.03.004.
Notes: All four reviewed items are journal articles published in 2024–2026 by Elsevier. Conference papers are excluded from the survey in accordance with the supplied college guidelines.

## Slide 11
THANK YOU
Notes: ap